## Slide 1: Unit - 1 Introduction to 8086 Processor

## Slide 2: Introduction
Intel introduced
    4004 – 4 bit processor – 1971
    8008 – 8 bit processor – 1972.
    These processor could not survive as general purpose due to design and performance limitations.
8080 – first general purpose 8 bit – 1974.
8085 followed 8080 – functionally complete processor.
Limitations of 8 bit processor
    low speed
    Low memory addressing capability.
    Limited no. of general purpose registers.
    Less powerful instruction set.
8086 – 16 bit processors.

## Slide 3: 1.1 REGISTER ORGANIZATION OF 8086
8086 has set of registers
    General Purpose Registers – 8 bit / 16 bit.
    Special purpose registers – 16 bit.
General purpose registers used for holding
    data
    Variables
    Intermediate results temporarily or for other purpose like counter or for storing offset address for some addressing modes.
Special purpose registers are used as
    segment registers
    Pointers
    Index registers or as offset storage registers for particular addressing modes.

## Slide 4: 1.1.1 General Data Registers
The registers AX, BX, CX, DX are general purpose 16 bit registers.
AX is used as 16 bit accumulator with
    AL – lower 8 bit.
    AH – higher 8 bit.
CX – used as default counter in the case of string and loop instructions.
BX – as an offset storage for forming physical addresses.
DX – as an implicit operand or destination in case of few instructions.
AH | AL
BH | BL
CH | CL
DH | DL
AX
BX
CX
DX

## Slide 5: 1.1.2 segment Registers
CS
SS
DS
ES
8086 addresses a segmented memory.
1MB memory is divided into 16 logical segments. Each segment contains 64 KB of memory.
    CS – Code Segment registers
    SS – Stack Segment registers
    DS – Data Segment registers
    ES – Extra Segment registers

## Slide 6: 1.1.2 segment Registers – Cond.
CS is used for addressing a memory location in the code segment of the memory, where the executable program is stored.
DS points to the data segment of the memory, where the data is resided.
ES refers to segment which is another segment of memory.
SS is used for addressing the stack segment of the memory which is used to store the stack data.

## Slide 7: 1.1.2 segment Registers – Cond.
CPU uses the stack for temporarily storing the data required at later stage.
The stack grows down. i.e. data is pushed onto the stack in the memory locations with decreasing address.
When this information is required by CPU, they will be popped off from the stack.
While addressing any location,
physical address = segment address + offset address

## Slide 8: 1.1.2 segment Registers – Cond.
Segment register – 16 bit segment base addresses.
Pointers and index or BX – offset address.
CS – segment address of code
DS – segment address of data.
SS – ,, ,, of stack.
ES - ,, ,, of extra segment of memory.

## Slide 9: 1.1.3 Pointers and Index Registers
SP
BP
SI
DI
IP
Pointers contain offset within particular segment.
IP, BP & SP contains offsets within the code (IP) and stack (BP & SP) segments.
Index registers – general purpose – for offset storage in case of indexed, base indexed and relative based indexed addressing modes.
SI – store the offset of source data in data segment.
DI – store the offset of destination in data or data segment.
Index registers – useful for string manipulation.

## Slide 10: 1.1.4 Flag Registers
Flag registers content indicate the result of computations in the ALU.
Also contains some flag bits to control the CPU operations.
FLAGS / PSW