## Slide 1: Digital to Analog Converters (DAC)

## Slide 2: What is a DAC?
A digital to analog converter (DAC) converts a digital signal to an analog voltage or current output.
DAC
100101…

## Slide 3: What is a DAC?
1011
1001
1010
0111
1000
0110
0101
0100
0011
0010
0001
0000
Digital Input Signal
Analog Output Signal

## Slide 4: Types of DACs
Many types of DACs available.
Usually switches, resistors, and op-amps used to implement conversion
Two Types:
  Binary Weighted Resistor
  R-2R Ladder

## Slide 5: Binary Weighted Resistor
Utilizes a summing op-amp circuit
Weighted resistors are used to distinguish each bit from the most significant to the least significant
Transistors are used to switch between Vref and ground (bit high or low)

## Slide 6: Binary Weighted Resistor
Assume Ideal Op-amp
No current into op-amp
Virtual ground at inverting input
Vout= -IRf
-
+
R
2R
4R
2nR
Rf
Vout
I
Vref

## Slide 7: Binary Weighted Resistor
MSB
LSB
Voltages V1 through Vn are either Vref if corresponding bit is high or ground if corresponding bit is low
V1 is most significant bit
Vn is least significant bit
I
-
+
R
2R
4R
2n-1R
Rf
Vout
Vref
V1
V2
V3
Vn

## Slide 8: Binary Weighted Resistor
If Rf=R/2
For example, a 4-Bit converter yields
Where b3 corresponds to Bit-3, b2 to Bit-2, etc.

## Slide 9: Binary Weighted Resistor
Advantages
  Simple Construction/Analysis
  Fast Conversion
Disadvantages
  Requires large range of resistors (2000:1 for 12-bit DAC) with necessary high precision for low resistors
  Requires low switch resistances in transistors
  Can be expensive. Therefore, usually limited to 8-bit resolution.