## Slide 1: Gated S-R Latch
S-R latch + enable input (EN) and 2 NAND gates  gated S-R latch.
S
R
Q
Q'
EN
S
EN
R
Q
Q'

## Slide 2: Gated D Latch
Make R input equal to S'  gated D latch.
D latch eliminates the undesirable condition of invalid state in the S-R latch.
D
EN
Q
Q'
D
Q
Q'
EN

## Slide 3: Gated D Latch
When EN is HIGH,
  D=HIGH  latch is SET
  D=LOW  latch is RESET
Hence when EN is HIGH, Q ‘follows’ the D (data) input.
Characteristic table:
When EN=1, Q(t+1) = D

## Slide 4: Edge-Triggered Flip-flops
Flip-flops: synchronous bistable devices
Output changes state at a specified point on a triggering input called the clock.
Change state either at the positive edge (rising edge) or at the negative edge (falling edge) of the clock signal.
Positive edges
Negative edges
Clock signal

## Slide 5: Edge-Triggered Flip-flops
S-R, D and J-K edge-triggered flip-flops. Note the “>” symbol at the clock input.
S
C
R
Q
Q'
S
C
R
Q
Q'
D
C
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
J
C
K
Q
Q'
Positive edge-triggered flip-flops
Negative edge-triggered flip-flops

## Slide 6: J-K Flip-flop
J-K flip-flop: Q and Q' are fed back to the pulse-steering NAND gates.
No invalid state.
Include a toggle state.
  J=HIGH (and K=LOW) a SET state
  K=HIGH (and J=LOW) a RESET state
  both inputs LOW a no change
  both inputs HIGH a toggle

## Slide 7: J-K Flip-flop
J-K flip-flop.
Characteristic table.
J
Q
Q'
CLK
Pulse transition detector
K
Q(t+1) = J.Q' + K'.Q

## Slide 8: T Flip-flop
T flip-flop: single-input version of the J-K flip flop, formed by tying both inputs together.
Characteristic table.
Q(t+1) = T.Q' + T'.Q
T
Q
Q'
CLK
Pulse transition detector
J
C
K
Q
Q'
CLK
T

## Slide 9: T Flip-flop
Application: Frequency division.
Application: Counter (to be covered in Lecture 13.)
J
C
K
Q
CLK
High
CLK
Q
Divide clock frequency by 2.
J
C
K
QA
CLK
High
J
C
K
QB
High
CLK
QA
QB
Divide clock frequency by 4.

## Slide 10: Asynchronous Inputs
S-R, D and J-K inputs are synchronous inputs, as data on these inputs are transferred to the flip-flop’s output only on the triggered edge of the clock pulse.
Asynchronous inputs affect the state of the flip-flop independent of the clock; example: preset (PRE) and clear (CLR) [or direct set (SD) and direct reset (RD)]
When PRE=HIGH, Q is immediately set to HIGH.
When CLR=HIGH, Q is immediately cleared to LOW.
Flip-flop in normal operation mode when both PRE and CLR are LOW.

## Slide 11: Asynchronous Inputs
A J-K flip-flop with active-LOW preset and clear inputs.
J
Q
Q'
CLK
Pulse transition detector
K
PRE
CLR
J
C
K
Q
Q'
PRE
CLR
PRE
CLR
CLK
Q
Preset
Toggle
Clear
J = K = HIGH