## Slide 1: Explanation
5. Indexed:
    In this mode, offset of the operand is stored in one of the index registers(DS is the default segment for index registers SI and DI)
    In case of string instructions DS and ES are default segment for index registers for SI and DI respectively.
    special case of register indirect addressing mode.
Ex:
MOV BX,[SI]
- data is available at an offset address stored in SI in DS.
Effective address = 10H * DS + [SI]

## Slide 2: 6.Register relative
    In this mode, data is available at an effective address formed by adding 8 – bit or 16 – bit displacement with the content of any one of the registers BX, BP, SI and DI in the default (either DS or ES) segment.
Ex:
MOV BX,50H[BX]
Effective address = 10H * DS + 50H+[BX]

## Slide 3: Explanation
7. Based Indexed:
    The effective address is formed, in this addressing mode, by adding content of a base register (BX / BP) to the content of index register (SI / DI).
    The default segment register may be ES or DS.
Ex:
MOV BX,[BX] [SI]
- BX is the base register and SI is the index register.
Effective address = 10H * DS + [BX] + [SI]

## Slide 4: Explanation
8. Relative Based Indexed:
    The effective address is formed by adding 8 or 16 bit displacement with the sum of contents of any one of the base registers (BX / BP) and any one of the index registers in a default segment.
Ex:
MOV BX,50H[BX] [SI]
- 50H is the immediate displacement, BX is the base register and SI is the index register.
Effective address = 10H * DS + 50H + [BX] + [SI]

## Slide 5: Addressing modes
Addressing modes for control transfer instructions are:
Modes for
Control
Transfer
Instructions
Intersegment
IntraSegment
Intersegment Direct
Intersegment Indirect
IntraSegment Direct
IntraSegment Indirect

## Slide 6: Control transfer instructions
IntraSegment Direct Mode:
      The address to which the control is to be transferred lies in the same segment in which the control transfer instructions lies and appears directly in the instructions as an immediate displacement value.
      The effective address to which the control is transferred is given by the sum of 8 or 16 bit displacement and current content of IP.
      In signed displacement: 8 bit i.e. -128< d < 127 – short jump.
      16 bit: -32768 < d < 32767 – long jump.
      Ex:
      JMP SHORT LABEL
      - LABEL lies within -128 to +127

## Slide 7: Control transfer instructions
2. IntraSegment Indirect Mode:
      The displacement to which the control is transferred, is in the same segment in which the control transfer instruction lies, but it is passed to the instruction indirectly.
      The branch address is the content of a register or a memory locations.
      This addressing mode may be used in unconditional branch instructions.
      Ex:
      JMP [BX]; jump to effective address stored in BX.