## Slide 1: 8255 interfacing problem

## Slide 2: Problem:
1. Find the control word if PA = out, PB = in, PC0 – PC3 = in, and PC4-PC7 = out.
    Control word = 1000 00112 = 83H
Ex. Program the 8255 to get data from port B and send it to port A. In addition, data from PCL is sent out to the PCU. Use port addresses of 300H-303H for the 8255 chip.

## Slide 3: Problem:
2. Program the 8255 to get data from port B and send it to port A. In addition, data from PCL is sent out to the PCU. Use port addresses of 300H-303H for the 8255 chip.
Given that:
In port: Port B, Port CL
Out Port: Port A, Port CU
Let us take 300H – Address of Port A
301H – Address of Port B
302H – Address of Port C
303 H – Address of Control word Register

## Slide 4
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
8 |  |  |  | 3 |  |  | 
Control word Value = 83 H
Program:
MOV AL, 83H ; Load control word value
OUT 303H, AL
MOV DX, 301H ; Load Port B address
IN AL, DX ; Get the data from Port B
OUT 300H, AL ; Transfer the data to Port A
MOV DX,302H ; Get the data from port C
IN AL, DX
AND AL, 0FH
ROL AL, 04H
OUT DX,AL ; Transfer the data to Port Cupper.
Control Word Register