## Slide 1: 1.2 ARCHITECTURE
Memory address and data bus interface
Internal Data Bus
Address Conversion Mechanism (adder)
CS
DS
SS
ES
IP
Internal Data Bus
AH | AL
BH | BL
CH | CL
DH | DL
SP | 
BP | 
SI | 
DI | 
ALU (16)
Flags (16)
Instruction byte
Queue 6 bytes
Decoding circuit
Timing & Control circuit
Clock& control signal
Address / status
A16 / S3 - A19 / S6
Address / Data
A D0 - A D15
BIU
EU

## Slide 2: 1.2 ARCHITECTURE – Cond.
It supports 16 bit ALU, a set of 16 bit registers.
It provides segmented memory addressing capability, rich instruction set, powerful interrupt structure, fetched instruction queue for overlapped fetching and execution etc.
The complete architecture of 8086 is subdivided into
    Bus Interface Unit (BIU)
    Execution Unit (EU)
BIU contains the circuit for physical calculations and a precoding instruction byte queue (6 bytes long).
BIU make the system’s bus signals available for external interfacing the devices. i.e. responsible for making communications with external devices and peripherals including memory via the bus.
The complete physical address – 20 bit long – generated using segment and offset registers each 16 bit long.

## Slide 3: Problem
If the segment address is 1005 H, offset address is 5555 H then calculate the physical address.
Solution:
Segment address = 1005 H
Offset address = 5555 H
Segment address=1005 H ->0001 0000 0000 0101
Shifted by 4 position -> 0001 0000 0000 0101 0000
+
Offset address -> 0101 0101 0101 0101
Physical addrs -> 0001 0101 0101 1010 0101
1 5 5 A 5

## Slide 4: Explanation
Segment value = 1005 H
Offset value = 0000 H – FFFF H
i.e. maximum value = 64 k
Thus segment register indicates the base address of a particular segment.
Offset indicates the distance of the memory location in the segment from the base address.
BIU has separate adder to perform this procedure for obtaining the physical address.
In 8085, while the opcode is fetched and decoded, the external bus is free for some time, while the processor internally executes the instruction.
This time slot is utilized in 8086 to achieve the overlapped fetch and execution cycles.
While the fetched instruction is executed internally, the external bus is used to fetch the machine code of next instruction and arrange it in a queue known as precoded instruction byte queue.
It is 6 bytes long, First – in – First – out structure.
From this instructions are taken sequentially for decoding.

## Slide 5: Explanation – Cond.
Once a byte is decoded, the queue is rearranged by pushing it out and status of queue is checked for the possibility of next code fetch cycle.
While the opcode is fetched by BIU, the EU executes the previously decoded instruction concurrently.
BUI along with EU forms the pipeline.
BUI manages the complete interface of EU with memory and I/O devices under the control of timing and control unit.
EU contains the register set except segment registers and IP.
It has 16 – bit ALU.
16 bit flag register reflects the result of execution by ALU.
Decoding unit – decodes the opcode bytes issued from the instruction byte queue.
Timing and control unit derives the necessary control signal to execute the instructions.
EU may pass the result to BIU for storing them in memory.

## Slide 6: 1.2.1 Memory segmentation
0000 64 KB FFFF
0000 64 KB FFFF
0000
1000
PHYSICAL MEMORY
Segment 1
Segment 2
CS 1
Offset IP1
CS 2
Offset IP2
2500
0000 1A00 64 KB
0000, 1A01 FFFF 64 KB
FFFF
0000
1000
PHYSICAL MEMORY
CS 1
Offset IP1
CS 2
Offset IP2
Non-overlapping segments
Overlapping segments
Segment 1
Segment 2
Overlap

## Slide 7: 1.2.1 Memory Segmentation – Cond.
Memory in 8086 / 8080 – segmented memory.
Complete memory is divided into number of logical segments.
Each segment is 64 k bytes.
Segment register points the starting location of a particular segments.
To address the specific memory location within the segment – need offset address.
Offset address – 16 bit long.
Maximum offset value – FFFF H.
Maximum size of segment – 64 KB.
The CPU 8086 is able to address 1 Mbytes of physical memory.
Complete 1 Mbytes memory is divided into 16 segments, each of 64 Kbytes size.
Segment address : 0000 H – F000 H.
Offset address : 0000 H – FFFF H.
This is called as non - overlapping segments.
If another segment starts before this 64 Kbytes locations of the first segment, the two segments are said to be called overlapped segment area.
The locations lying in the overlapped area may be addressed by the same physical address generated from two different sets of segment and offset address.

## Slide 8: 1.2.1 Memory Segmentation – Cond.
The main advantages of the segment memory scheme are:
    Allows the memory capacity to be 1 Mbytes although the actual addresses to be handled are of 16 – bit size.
    Allows the placing of code, data and stack portions of the same program in different parts of memory, for data and code protection.
    Permits a program and / or its data to be put into different areas of memory each time the program is executed. i.e. provision for relocation is done.
In overlapped system
    Physical address = CS1+IP1=CS2+IP2
    ‘+’ indicates the procedure of physical address information.