## Slide 1: Flag Registers

## Slide 2: Flag Registers
Flag registers content indicate the result of computations in the ALU.
Also contains some flag bits to control the CPU operations.
FLAGS / PSW

## Slide 3: 1.2.1 Flag Register
X | X | X | X | O | D | I | T | S | Z | X | AC | X | P | X | CY
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
O – Overflow flag
D – Direction flag
I – Interrupt flag
T – Trag flag
S – Sign flag
Z – Zero flag
AC – Auxiliary flag
P – Parity flag
CY – Carry flag
X – Not used

## Slide 4: 1.2.1 Flag Register – Cond..
8086 has 16 bit flag register which is divided into two parts:
    Condition code / status flag
    Machine control flags
Condition code flag register is the lower byte of the 16 bit flag register along with the overflow flag.
This flag is identical to 8085 flag register, with an additional overflow flag, which is not present in 8085.
Flag register reflects the operations performed by ALU.
Control flag register is the higher byte of the flag register of 8086.
It contains 3 flags:
    Direction flag (D).
    Interrupt flag (I).
    Trap flag (T).
S – sign flag: 1- result of any computation is negative.
For signed computations, the sign flag equals to the MSB of the result.
Z – zero flag : 1 – result of the computation or comparision performed by instruction is zero.

## Slide 5: 1.2.1 Flag Register – Cond..
P – Parity flag : 1 – if the lower byte of the result contains even number of 1s.
C – Carry Flag: it is set when there is a carry out of MSB in the case of addition or a borrow in the case of subtraction.
T – Trap flag: if this flag is set, the processor enters the single step execution mode. In other words, a trap interrupt is generated after execution of each instruction.
I – Interrupt flag: if this flag is set, the maskable interrupt are recognized by the CPU, otherwise they are ignored.
Direction flag: used by string manipulation instructions.
0 – the string is processed beginning from the lowest address to highest address. (autoincrementing mode).
1 – the string is processed beginning from the highest address to lowest address. (autodecrementing mode).
AC – Auxiliary carry flag: it is set if there is carry/borrow from lowest nibble during addition / subtraction.
O – Overflow flag: it is set, if overflows occurs.