## Slide 1: 8086 – instruction set

## Slide 2: Types of 8086 instructions
Data transfer
Arithmetic and logical
Control transfer
miscellaneous instructions

## Slide 3: Data transfer
MOV dest, src; move Byte or word
Flags Affected: None
Copies the byte or word from source operand to destination operand.
Register to register operation:
    MOV AX, BX
    MOV BX, AX
    MOV DX,CX
    MOV CX,AX

## Slide 4: Data transfer
Memory to Register operation:
MOV AX, [5000H]
MOV BX, [2500H]
Register to Memory Operation:
MOV [5000H], AX
MOV [2500H],BX
Immediate Data to Register operation:
MOV AX, 1234H
MOV BX, 0A2C0H
MOV CX, 0FFFFH

## Slide 5: Data transfer
Immediate Data to Memory operation:
MOV [2500H], 1234H
MOV [5000H], 0FFFFH
MOV [1234H], 0A123H
Register to Segment Register operation:
MOV DS, AX
MOV CS, BX
MOV SS, AX
Segment Register to Register operation:
MOV AX, DS
MOV BX, CS
MOV AX, SS

## Slide 6: Data transfer
Memory to Accumulator operation(DIRECT ADDRESSING):
MOV AL, [5000H]
MOV AX, [5000H]
Accumulator to Memory operation(DIRECT ADDRESSING):
MOV [5000h], AL
MOV [5000h], AX

## Slide 7: Data transfer
Stack Operation:
    PUSH
    POP
    PUSHF
    LDS
    LEA
    LES
    LODSB/LODSW
    STOSB/ STOSW
    MOVSB/MOVSW
    REP
    REPE/ REPZ
    REPNE/ REPNZ
    LAHF
    SAHF
    XCHG
    XLAT
    IN / INW PORT
    OUT / OUTW PORT

## Slide 8: STACK OPERATION
PUSH:
PUSH AX push the content of AX to Stack
12
34
1234
SP
AX
AH
AL
00
00
AX
AH
AL
stack

## Slide 9: STACK OPERATION
POP:
POP AX – pop the content of Stack to AX
00
00
SP
AX
AH
AL
12
34
AX
AH
AL
stack