## Slide 1: Arithmetic group
Addition, subtraction, multiplication & division of binary numbers.
Addition, subtraction, multiplication & division of ASCII or unpacked BCD numbers.
Increment & decrement operations.
Comparison of two bytes.
ADD dest, src – Arithmetic Addition
Register to register operation:
ADD AX, BX – 16 BIT ADDITION
ADD AL, BL – 8 BIT ADDITION

## Slide 2: ADD dest, src – Arithmetic Addition
Register to memory location:
ADD [5000H], AX
ADD [5000H], AL
memory to Register location:
ADD AX, [5000H]
ADD AL, [5000H]
Immediate data to register operation:
ADD AX, 0A234H
ADD AL, 0A2H
ADD BX, 1234H

## Slide 3: ADD dest, src – Arithmetic Addition
Immediate data to memory operation:
ADD [5000H], 0A234H
ADD [2500H], 0A2H
ADD [1234H], 1234H
ADC dest, src – Add with Carry
Register to register operation:
ADC AX, BX – 16 BIT ADDITION
ADC AL, BL – 8 BIT ADDITION

## Slide 4
Register to memory location:
ADC [5000H], AX
ADC [5000H], AL
memory to Register location:
ADC AX, [5000H]
ADC AL, [5000H]
Immediate data to register operation:
ADC AX, 0A234H
ADC AL, 0A2H
ADC BX, 1234H

## Slide 5
Immediate data to memory operation:
ADC [5000H], 0A234H
ADC [2500H], 0A2H
ADC [1234H], 1234H

## Slide 6: SUB dest, src - Subtract
Register from register operation:
SUB AX, BX – 16 BIT ADDITION
SUB AL, BL – 8 BIT ADDITION
Immediate data from register operation:
SUB AX, 0A234H
SUB AL, 0A2H
SUB BX, 1234H
Register from memory location:
SUB [5000H], AX
SUB [5000H], AL

## Slide 7: SUB dest, src - Subtract
memory from Register location:
SUB AX, [5000H]
SUB AL, [5000H]
Immediate data from memory operation:
SUB [5000H], 0A234H
SUB [2500H], 0A2H
SUB [1234H], 1234H