## Slide 1: Addressing modes

## Slide 2: Introduction
A way of locating data or operands.
Depending upon the data types used in the instruction and the memory addressing modes, any instruction may belong to one or more addressing modes.
Addressing modes describes the type of operands and the way they are accessed for executing an instruction.
According to flow of instruction execution, the instruction may be classified as
(i) sequential control flow instruction
(ii) control transfer instruction.

## Slide 3: Introduction ….
Sequential control flow instructions are the instructions which transfer its control to immediate next instructions.
For ex: arithmetic, logical, data transfer and process control instructions.
Control transfer instructions transfer its control to some predefined address.
For ex: INT , CALL, RET and JUMP

## Slide 4: Addressing modes
Addressing modes for sequential transfer instructions are:
Immediate
Direct
Register
Register indirect
Indexed
Register relative
Based indexed
Relative based indexed

## Slide 5: Explanation
Immediate:
immediate data is part of instruction, and appears in the form of successive byte or bytes.
Ex:
MOV AX, 0005H
- 0005H is the immediate data.
- it may 8 bit/16 bit in size.

## Slide 6: Explanation
2. Direct:
a 16 bit memory address (offset) is directly specified in the instruction as a part of it.
Ex:
MOV AX, [5000H]
- here data resides in the memory locations in the data segment, whose effective address may be calculated using 5000H as the offset address and content of DS as segment address.
Effective address = 10H*DS + 5000H

## Slide 7: Explanation
3. Register:
Data is stored in a register and it is referred using particular register. All the registers, except IP, may be used in this mode.
Ex:
MOV BX,AX

## Slide 8: Explanation
4. Register Indirect:
    The address of memory location which contains data or operand is determined in an indirect way, using offset registers.
    In this mode, the offset address of data is either in BX or SI or DI register.
    the default segment is either DS or ES.
Ex:
MOV AX,[BX]
- data present in a memory location in DS whose offset address is in BX.
Effective address = 10H * DS + [BX]