## Slide 1: Introduction: Registers
An n-bit register has a group of n flip-flops and some logic gates and is capable of storing n bits of information.
The flip-flops store the information while the gates control when and how new information is transferred into the register.
Some functions of register:
  retrieve data from register
  store/load new data into register (serial or parallel)
  shift the data within register (left or right)

## Slide 2: Simple Registers
No external gates.
Example: A 4-bit register. A new 4-bit data is loaded every clock cycle.
A3
CP
A1
A0
D
Q
D
Q
Q
D
A2
D
Q
I3
I1
I0
I2

## Slide 3: Shift Registers
Another function of a register, besides storage, is to provide for data movements.
Each stage (flip-flop) in a shift register represents one bit of storage, and the shifting capability of a register permits the movement of data from stage to stage within the register, or into or out of the register upon application of clock pulses.

## Slide 4: Shift Registers
Basic data movement in shift registers (four bits are used for illustration).
Data in
Data out
(a) Serial in/shift right/serial out
Data in
Data out
(b) Serial in/shift left/serial out
Data in
Data out
(c) Parallel in/serial out
Data out
Data in
(d) Serial in/parallel out
Data out
Data in
(e) Parallel in / parallel out
(f) Rotate right
(g) Rotate left

## Slide 5: Serial In/Serial Out Shift Registers
Accepts data serially – one bit at a time – and also produces output serially.
Q0
CLK
D
C
Q
Q1
Q2
Q3
Serial data input
Serial data output
D
C
Q
D
C
Q
D
C
Q

## Slide 6: Serial In/Serial Out Shift Registers
Application: Serial transfer of data from one register to another.
Shift register A
Shift register B
SI
SI
SO
SO
Clock
Shift control
CP
Wordtime
T1
T2
T3
T4
CP
Clock
Shift control

## Slide 7: Serial In/Serial Out Shift Registers
Serial-transfer example.

## Slide 8: Serial In/Parallel Out Shift Registers
Accepts data serially.
Outputs of all stages are available simultaneously.
Q0
CLK
D
C
Q
Q1
D
C
Q
Q2
D
C
Q
Q3
D
C
Q
Data input
D
C
CLK
Data input
Q0
Q1
Q2
Q3
SRG 4
Logic symbol

## Slide 9: Parallel In/Serial Out Shift Registers
Bits are entered simultaneously, but output is serial.
D0
CLK
D
C
Q
D1
D
C
Q
D2
D
C
Q
D3
D
C
Q
Data input
Q0
Q1
Q2
Q3
Serial data out
SHIFT/LOAD
SHIFT.Q0 + SHIFT'.D1

## Slide 10: Parallel In/Serial Out Shift Registers
Bits are entered simultaneously, but output is serial.
Logic symbol
C
CLK
SHIFT/LOAD
D0
D1
D2
D3
SRG 4
Serial data out
Data in

## Slide 11: Parallel In/Parallel Out Shift Registers
Simultaneous input and output of all data bits.
Q0
CLK
D
C
Q
Q1
D
C
Q
Q2
D
C
Q
Q3
D
C
Q
Parallel data inputs
D0
D1
D2
D3
Parallel data outputs

## Slide 12: Bidirectional Shift Registers
Data can be shifted either left or right, using a control line RIGHT/LEFT (or simply RIGHT) to indicate the direction.
CLK
D
C
Q
D
C
Q
D
C
Q
D
C
Q
Q0
Q1
Q2
Q3
RIGHT/LEFT
Serial data in
RIGHT.Q0 + RIGHT'.Q2

## Slide 13: Bidirectional Shift Registers
4-bit bidirectional shift register with parallel load.
CLK
I4
I3
I2
I1
Serial input for shift-right
D
Q
D
Q
D
Q
D
Q
Clear
4x1 MUX
s1
s0
3 2 1 0
4x1 MUX
3 2 1 0
4x1 MUX
3 2 1 0
4x1 MUX
3 2 1 0
A4
A3
A2
A1
Serial input for shift-left
Parallel inputs
Parallel outputs

## Slide 14: Bidirectional Shift Registers
4-bit bidirectional shift register with parallel load.

## Slide 15: An Application – Serial Addition
Most operations in digital computers are done in parallel. Serial operations are slower but require less equipment.
A serial adder is shown below. A  A + B.
FA
x
y
z
S
C
Shift-register A
Shift-right
CP
SI
Shift-register B
SI
External input
SO
SO
Q
D
Clear

## Slide 16: An Application – Serial Addition
A = 0100; B = 0111. A + B = 1011 is stored in A after 4 clock pulses.
Initial:
A: 0 1 0 0
B: 0 1 1 1
Q: 0
Step 1: 0 + 1 + 0
S = 1, C = 0
A: 1 0 1 0
B: x 0 1 1
Q: 0
Step 2: 0 + 1 + 0
S = 1, C = 0
A: 1 1 0 1
B: x x 0 1
Q: 0
Step 3: 1 + 1 + 0
S = 0, C = 1
A: 0 1 1 0
B: x x x 0
Q: 1
Step 4: 0 + 0 + 1
S = 1, C = 0
A: 1 0 1 1
B: x x x x
Q: 0

## Slide 17: Shift Register Counters
Shift register counter: a shift register with the serial output connected back to the serial input.
They are classified as counters because they give a specified sequence of states.
Two common types: the Johnson counter and the Ring counter.

## Slide 18: Ring Counters
One flip-flop (stage) for each state in the sequence.
The output of the last stage is connected to the D input of the first stage.
An n-bit ring counter cycles through n states.
No decoding gates are required, as there is an output that corresponds to every state the counter is in.

## Slide 19: Ring Counters
Example: A 6-bit (MOD-6) ring counter.
CLK
Q0
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Q1
Q2
Q3
Q4
Q5
CLR
PRE
100000
010000
001000
000100
000010
000001

## Slide 20: Johnson Counters
The complement of the output of the last stage is connected back to the D input of the first stage.
Also called the twisted-ring counter.
Require fewer flip-flops than ring counters but more flip-flops than binary counters.
An n-bit Johnson counter cycles through 2n states.
Require more decoding circuitry than ring counter but less than binary counters.

## Slide 21: Johnson Counters
Example: A 4-bit (MOD-8) Johnson counter.
CLK
Q0
D
Q
D
Q
D
Q
D
Q
Q1
Q2
Q3'
CLR
Q'
0000
0001
0011
0111
1111
1110
1100
1000

## Slide 22: Johnson Counters
Decoding logic for a 4-bit Johnson counter.
A'
D'
State 0
A
D
State 4
B
C'
State 2
C
D'
State 3
A
B'
State 1
A'
B
State 5
B'
C
State 6
C'
D
State 7