## Slide 1: Cache memory
If the active portions of the program and data are placed in a fast small memory the average memory access time can be reduced ,thus reducing the total execution time of the program.
Such fast small memory is referred to cache memory.
It is placed between the CPU and main memory .
CM access time is less than access time of MM hierarchy by a factor 5 to 10.
The cache is the fastest component in the memory hierarchy and approaches the speed of components.

## Slide 2
operation of the cache: If the word is found in the cache ,it read from the fast memory.
If the word addressed by the CPU is not found in the cache, the main memory is accessed to read the word.
A block of words containing the one just accessed is then transferred from main memory to cache memory.

## Slide 3
Hit ratio:
The performance of cache memory is frequently measured in terms of a quantity called hit ratio.
When the CPU refers to memory an finds the word in cache, is said hit.
If the word is not found in cache, it is in main memory and it count as miss.
The ratio of the number of hits divided by the total CPU references to memory (hits plus misses) is the hit ratio.
The basic characteristic of cache memory is fast access time. Therefore very little or no time must be wasted when searching for words in the cache .
The transformation of data from main memory to cache memory is referred as mapping process

## Slide 4: Mapping Process
Associative mapping
Direct mapping
Set-associative mapping
Ex
Main memory
32KX12
Cache
512 X 12
CPU

## Slide 5: Associative mapping
Associative mapping cache
Address(15 bit)
Data(12 bit)
Argument reg
CPU address(15)
01000
02777
22345
3450
6710
1234

## Slide 6
The associative memory stores both address and content (data) of the memory word. This permits any location cache to store any word from main memory .
Address-15 and data-12.
A CPU address of 15 bits placed in the argument register and associative memory is searched for a matching address.
If address is found, the corresponding 12 bit data is read and sent to the CPU.
If no match occurs the main memory is accessed for the word. the address data pair is then transferred to the associative cache memory. If the cache is full an address data pair must be displaced to make room for a pair that is needed and not presently in the cache.

## Slide 7: Direct mapping
Associative memories are expensive compared to random-access memories because of the added logic associated with each cell.
index
tag
6 bits
9 bits
32 K X 12
Main memory
Address=15 bits
Data = 12 bits
512 X 12
Cache memory
Address=9 bits
Data=12 bits
000
777
00 000
77 777

## Slide 8
2(k) words in cache memory 2(n) MM
N bit divided into two fields k bits index and n-k bits for tag field.
00
1220
tag
data
Index add
000
777
02
6710
Memory add
00000
1220
00777
2340
02000
5670
02777
6710
Main memory
Cache memory

## Slide 9: DIRECT MAPPING
Direct Mapping with block size of 8 words
Index
tag
data
000
0 1
3 4 5 0
007
0 1
6 5 7 8
010
017
770
0 2
777
0 2
6 7 1 0
Block 0
Block 1
Block 63
Tag Block Word
6
6
3
INDEX
Cache Memory

## Slide 10
Set Associative Mapping Cache with set size of two
Index
Tag
Data
000
0 1
3 4 5 0
0 2
5 6 7 0
Tag
Data
777
0 2
6 7 1 0
0 0
2 3 4 0

## Slide 11: Set associative mapping
Replacement algorithm
When a miss occurs in a set-associative cache and set is full ,it is necessary to replace one of tag-data items with a new value. Most common replacement algorithm used (FIFO) and least recently used (LRU).
With random replacement policy, control choose one tag-data item for replacement at random.
FIFO procedure selects for replacement the item that has been in the set the longest.
LRU algorithm selects for replacement the item that has been least recently used by CPU.

## Slide 12: CACHE WRITE or WRITE POLICIES
Write Through
When writing into memory
If Hit, both Cache and memory is written in parallel
If Miss, Memory is written
For a read miss, missing block may be
overloaded onto a cache block
Memory is always updated
-> Important when CPU and DMA I/O are both executing
Slow, due to the memory access time
Write-Back (Copy-Back)
When writing into memory
If Hit, only Cache is written
If Miss, missing block is brought to Cache and write into Cache
For a read miss, candidate block must be
written back to the memory
Memory is not up-to-date, i.e., the same item in
Cache and memory may have different value
Cache Memory

## Slide 13
Cache initialization.
Cache is initialized when power is applied to the computer on when main memory is loaded with a complete set of program from auxiliary memory .
After initialization the cache is considered to be empty but in effect it contains some non valid data indicate each word in cache a valid but to indicate whether or not the word contains valid data cache it initialized by clearing all valid bits to 0 valid bit of a particular cache word is set to 1 the first time this word is loaded from main memory and stays set unless the cache has to be initialized again.

## Slide 14
A digital computer has a memory unit of 64 K X 16 and a cache memory of 1K words. The cache uses direct mapping with a block size of four words.
  A) How many bits are there in tag, index, block and word fields of
  the address format?
b) How many bits are there in each word of cache and how are
they divided into functions? Include a valid bit.
c) How many blocks can the cache accommodate?
Problem -1

## Slide 15: SOLUTION
Memory capacity--- 64KX16
Cache capacity------1KX16
Direct mapping with block size ---4 word
a) Memory space=
Therefore words in memory
Therefore 16 bits are required to address the memory
Cache words
10 bits are register to address the cache
6 bits
10 bits
16 bits
tags
index

## Slide 16
Cache divided into blocks of 4 words
Number of blocks ---- = blocks
256 blocks
Tag
block
word
6 bits
8 bits
2 bits

## Slide 17
b) Tag bits + data word bits +valid bit
6 + 16 + 1-- 23 bits
Blocks =256 blocks
2) An address space is specified by 24 bits and coresponding memory space by 16 bits.
  How many words are there in the address space?
  How many words are there in the memory space?
  If a page consists of 2K words, how many pages and blocks are there in the system?
Address space—24 bits
memory space—16 bits
a) Words in address space –
b) Words in memory space --
c) Page size – 2K words
How many pages --- = = =8k
How many blocks------ = = = 32 blocks

## Slide 18: PROBLEM 3
How many 128 X 8 RAM chips are needed to provide a memory capacity of 2048 bytes?
  How many lines of the address bus must be used to access 2048 bytes of memory? How many of these lines will be common to all chips?
  How many lines must be decoded for chip select? Specify the size of the decoders?

## Slide 19: SOLN