## Slide 1: INPUT-OUTPUT ORGANIZATION
Peripheral Devices
Input-Output Interface
Asynchronous Data Transfer
Modes of Transfer
Priority Interrupt
Direct Memory Access
Input-Output Processor
Serial Communication

## Slide 2: PERIPHERAL DEVICES
Input Devices
Keyboard
Optical input devices
- Card Reader
- Paper Tape Reader
- Bar code reader
- Digitizer
- Optical Mark Reader
Magnetic Input Devices
- Magnetic Stripe Reader
Screen Input Devices
- Touch Screen
- Light Pen
- Mouse
Analog Input Devices
Output Devices
Card Puncher, Paper Tape Puncher
CRT
Printer (Impact, Ink Jet,
Laser, Dot Matrix)
Plotter
Analog
Voice
Peripheral Devices

## Slide 3: INPUT/OUTPUT INTERFACE
Input/Output Interfaces
Provides a method for transferring information between internal storage (such as memory and CPU registers) and external I/O devices
Resolves the differences between the computer and peripheral devices
  Peripherals - Electromechanical Devices
  CPU or Memory - Electronic Device
  Data Transfer Rate
    Peripherals - Usually slower
    CPU or Memory - Usually faster than peripherals
      Some kinds of Synchronization mechanism may be needed
  Unit of Information
    Peripherals – Byte, Block, …
    CPU or Memory – Word
  Data representations may differ

## Slide 4: I/O BUS AND INTERFACE MODULES
Each peripheral has an interface module associated with it
Interface
- Decodes the device address (device code)
- Decodes the commands (operation)
- Provides signals for the peripheral controller
- Synchronizes the data flow and supervises
the transfer rate between peripheral and CPU or Memory
Typical I/O instruction
(Command)
Op. code
Device address
Function code
Input/Output Interfaces
Processor
Interface
Keyboard
and
display
terminal
Magnetic
tape
Printer
Interface
Interface
Interface
Data
Address
Control
Magnetic
disk
I/O bus

## Slide 5: TYPE OF COMMAND
CONTROL
STATUS
DATA O/P
DATA I/P
Control command to activate the peripheral and to inform it what to do
Ex magnetic tape unit instructed to backspace the tape by one record.
Status : to test various status conditions in the interface and peripheral.
Ex check status of peripheral before a transfer is initiated.
o/p data: causes interfaces to respond by transferring data from bus into one of its registers
i/p data: interface receives an item of data from peripheral and places it in its buffer register .processor checks if data are available by means of status command and then issues a data i/p command. interface place data on data line after which they are accepted by processor

## Slide 6: I/O BUS AND MEMORY BUS
  MEMORY BUS is for information transfers between
  CPU and the MM
  * I/O BUS is for information transfers between CPU
  and I/O devices through their I/O interface
3 ways comm. memory and i/o
use 2 separate buses one for memory and other for i/o
Use one common bus for both memory and i/o but have separate control
line for each.
Use one common bus for memory and i/o with common control line.
IOP
computer has independent set of data ,address and control bus one for
accessing memory and other for I/O. This can be done by IOP and CPU.
The memory comm with both CPU and IOP through a memory bus.
The IOP comm also with input and output device through separate I/O bus its
own address ,data and control line.
The purpose of IOP is to provide an independent pathway for transfer of
information between external device and internal memory
Input/Output Interfaces

## Slide 7: ISOLATED vs MEMORY MAPPED I/O
- Separate I/O read/write control lines in addition to memory read/write control lines
- Separate (isolated) memory and I/O address spaces
- Distinct input and output instructions
Isolated I/O
Memory-mapped I/O
  - A single set of read/write control lines
  (no distinction between memory and I/O transfer)
  - Memory and I/O addresses share the common address space
  -> reduces memory address range available
  - No specific input or output instruction
  -> The same memory reference instructions can
  be used for I/O transfers
  - Considerable flexibility in handling I/O operations
Input/Output Interfaces

## Slide 8: I/O INTERFACE
- Information in each port can be assigned a meaning
depending on the mode of operation of the I/O device
→ Port A = Data; Port B = Command; Port C = Status
- CPU initializes(loads) each port by transferring a byte to the Control Register
→ Allows CPU can define the mode of operation of each port
→ Programmable Port: By changing the bits in the control register, it is
possible to change the interface characteristics
CS RS1 RS0 Register selected
0 x x None - data bus in high-impedence
1 0 0 Port A register
1 0 1 Port B register
1 1 0 Control register
1 1 1 Status register
Programmable Interface
Input/Output Interfaces
Chip select
Register select
Register select
I/O read
I/O write
CS
RS1
RS0
RD
WR
Timing
and
Control
Bus
buffers
Bidirectional
data bus
Port A
register
Port B
register
Control
register
Status
register
I/O data
I/O data
Control
Status
Internal bus
CPU
I/O
Device

## Slide 9: ASYNCHRONOUS DATA TRANSFER
Synchronous - All devices derive the timing
information from common clock line
Asynchronous - No common clock
Asynchronous data transfer between two independent units requires that
control signals be transmitted between the communicating units to
indicate the time at which data is being transmitted
Strobe pulse
- A strobe pulse is supplied by one unit to indicate
the other unit when the transfer has to occur
Handshaking
- A control signal is accompanied with each data
being transmitted to indicate the presence of data
- The receiving unit responds with another control
signal to acknowledge receipt of the data
Synchronous and Asynchronous Operations
Asynchronous Data Transfer
Two Asynchronous Data Transfer Methods
Asynchronous Data Transfer

## Slide 10: STROBE CONTROL
* Employs a single control line to time each transfer
* The strobe may be activated by either the source or
the destination unit
Source
unit
Destination
unit
Data bus
Strobe
Data
Strobe
Valid data
Block Diagram
Timing Diagram
Source-Initiated Strobe
for Data Transfer
Source
unit
Destination
unit
Data bus
Strobe
Data
Strobe
Valid data
Block Diagram
Asynchronous Data Transfer
Destination-Initiated Strobe
for Data Transfer
Timing Diagram

## Slide 11: HANDSHAKING
Strobe Methods
Source-Initiated
The source unit that initiates the transfer has
no way of knowing whether the destination unit
has actually received data
Destination-Initiated
The destination unit that initiates the transfer
no way of knowing whether the source has
actually placed the data on the bus
To solve this problem, the HANDSHAKE method
introduces a second control signal to provide a Reply
to the unit that initiates the transfer
Asynchronous Data Transfer

## Slide 12: SOURCE-INITIATED TRANSFER USING HANDSHAKE
* Allows arbitrary delays from one state to the next
* Permits each unit to respond at its own data transfer rate
* The rate of transfer is determined by the slower unit
Block Diagram
Timing Diagram
Accept data from bus.
Enable data accepted
Disable data accepted.
Ready to accept data
(initial state).
Sequence of Events
Place data on bus.
Enable data valid.
Source unit
Destination unit
Disable data valid.
Invalidate data on bus.
Source
unit
Destination
unit
Data bus
Data accepted
Data bus
Data valid
Valid data
Data valid
Data accepted
Asynchronous Data Transfer

## Slide 13: DESTINATION-INITIATED TRANSFER USING HANDSHAKE
* Handshaking provides a high degree of flexibility and reliability because the
successful completion of a data transfer relies on active participation by both units
* If one unit is faulty, data transfer will not be completed
-> Can be detected by means of a timeout mechanism
Block Diagram
Timing Diagram
Source
unit
Destination
unit
Data bus
Ready for data
Data valid
Sequence of Events
Place data on bus.
Enable data valid.
Source unit
Destination unit
Ready to accept data.
Enable ready for data.
Disable data valid.
Invalidate data on bus
(initial state).
Accept data from bus.
Disable ready for data.
Ready for data
Data valid
Data bus
Valid data
Asynchronous Data Transfer

## Slide 14: Asynchronous serial transfer
In Serial data transfer each bit in the message is sent in sequence one at a time. Serial transmission is slower but less expensive.
Serial transmission types:1)Synchronous 2)Asynchronous
Syn: Two units share a common clock frequency and bits are transmitted continuously at the rate of clock pulse.
Asy: binay infor is sent only when it is available and the line remain idle when there is no information to be transmitted.

## Slide 15: ASYNCHRONOUS SERIAL TRANSFER
Asynchronous serial transfer
Synchronous serial transfer
Asynchronous parallel transfer
Synchronous parallel transfer
- Employs special bits which are inserted at both
ends of the character code
- Each character consists of three parts; Start bit; Data bits; Stop bits.
A character can be detected by the receiver from the knowledge of 4 rules;
- When data are not being sent, the line is kept in the 1-state (idle state)
- The initiation of a character transmission is detected
by a Start Bit , which is always a 0
- The character bits always follow the Start Bit
- After the last character , a Stop Bit is detected when
the line returns to the 1-state for at least 1 bit time
The receiver knows in advance the transfer rate of the
bits and the number of information bits to expect
Four Different Types of Transfer
Asynchronous Serial Transfer
Start
bit
(1 bit)
Stop
bits
Character bits
1
1
0
0
0
1
0
1
(at least 1 bit)
Asynchronous Data Transfer

## Slide 16: FIRST-IN-FIRST-OUT(FIFO) BUFFER
* Input data and output data at two different rates
* Output data are always in the same order in which the data entered the buffer.
* Useful in some applications when data is transferred asynchronously
4 x 4 FIFO Buffer (4 4-bit registers Ri),
4 Control Registers(flip-flops Fi, associated with each Ri)
Asynchronous Data Transfer
4-bit
register
S
R
F
F'
1
1
4-bit
register
S
R
F
F'
2
2
4-bit
register
S
R
F
F'
3
3
4-bit
register
S
R
F
F'
4
4
F
F
S
R
F
F'
S
R
Clock
Clock
Clock
Clock
Data
output
Output
ready
Delete
Data
input
Insert
Input ready
Master clear
R1
R2
R3
R4

## Slide 17: MODES OF TRANSFER - PROGRAM-CONTROLLED I/O -
3 different Data Transfer Modes between the central
computer(CPU or Memory) and peripherals;
Program-Controlled I/O
Interrupt-Initiated I/O
Direct Memory Access (DMA)
Program-Controlled I/O(Input Dev to CPU)
Modes of Transfer
Polling or Status Checking
Continuous CPU involvement
CPU slowed down to I/O speed
Simple
Least hardware
Read status register
Check flag bit
flag
Read data register
Transfer data to memory
Operation
complete?
Continue with
program
= 0
= 1
yes
no
CPU
Data bus
Address bus
I/O read
I/O write
Interface
Data register
Status
register
F
I/O bus
Data valid
Data accepted
I/O
device

## Slide 18: MODES OF TRANSFER - INTERRUPT INITIATED I/O & DMA
DMA (Direct Memory Access)
- Large blocks of data transferred at a high speed to
or from high speed devices, magnetic drums, disks, tapes, etc.
- DMA controller
Interface that provides I/O transfer of data directly
to and from the memory and the I/O device
- CPU initializes the DMA controller by sending a
memory address and the number of words to be transferred
- Actual transfer of data is done directly between
the device and memory through DMA controller
-> Freeing CPU for other tasks
  - Polling takes valuable CPU time
  - Open communication only when some data has
  to be passed -> Interrupt.
  - I/O interface, instead of the CPU, monitors the I/O device
  - When the interface determines that the I/O device is
  ready for data transfer, it generates an Interrupt Request to the CPU
  - Upon detecting an interrupt, CPU stops momentarily
  the task it is doing, branches to the service routine
  to process the data transfer, and then returns to the
  task it was performing
Interrupt Initiated I/O
Modes of Transfer

## Slide 19: PRIORITY INTERRUPT
Priority Interrupt by Software(Polling)
- Priority is established by the order of polling the devices(interrupt sources)
- Flexible since it is established by software
- Low cost since it needs a very little hardware
- Very slow
Priority Interrupt by Hardware
- Require a priority interrupt manager which accepts
all the interrupt requests to determine the highest priority request
- Fast since identification of the highest priority
interrupt request is identified by the hardware
- Fast since each interrupt source has its own interrupt vector to access
directly to its own service routine
Priority
- Determines which interrupt is to be served first
when two or more requests are made simultaneously
- Also determines which interrupts are permitted to
interrupt the computer while another is being serviced
- Higher priority interrupts can make requests while
servicing a lower priority interrupt
Priority Interrupt

## Slide 20: HARDWARE PRIORITY INTERRUPT - DAISY-CHAIN -
One stage of the daisy chain priority arrangement
PI RF PO Enable
0 0 0 0
0 1 0 0
1 0 1 0
1 1 1 1
Interrupt Request from any device(>=1)
-> CPU responds by INTACK <- 1
-> Any device receives signal(INTACK) 1 at PI puts the VAD on the bus
Among interrupt requesting devices the only device which is physically closest
to CPU gets INTACK=1, and it blocks INTACK to propagate to the next device
Priority Interrupt
Device 1
PI
PO
Device 2
PI
PO
Device 3
PI
PO
INT
INTACK
Interrupt request
Interrupt acknowledge
To next
device
CPU
VAD 1
VAD 2
VAD 3
Processor data bus
* Serial hardware priority function
* Interrupt Request Line
- Single common line
* Interrupt Acknowledge Line
- Daisy-Chain
S
R
Q
Interrupt
request
from device
PI
Priority in
RF
Delay
Vector address
VAD
PO
Priority out
Interrupt request to CPU
Enable

## Slide 21: PARALLEL PRIORITY INTERRUPT
IEN: Set or Clear by instructions ION or IOF
IST: Represents an unmasked interrupt has occurred. INTACK enables
tristate Bus Buffer to load VAD generated by the Priority Logic
Interrupt Register:
- Each bit is associated with an Interrupt Request from
different Interrupt Source - different priority level
- Each bit can be cleared by a program instruction
Mask Register:
- Mask Register is associated with Interrupt Register
- Each bit can be set or cleared by an Instruction
Priority Interrupt
Mask
register
INTACK
from CPU
Priority
encoder
I
0
I
1
I
2
I
3
0
1
2
3
y
x
IST
IEN
0
1
2
3
0
0
0
0
0
0
Disk
Printer
Reader
Keyboard
Interrupt register
Enable
Interrupt
to CPU
VAD
to CPU
Bus
Buffer

## Slide 22: INTERRUPT PRIORITY ENCODER
Determines the highest priority interrupt when
more than one interrupts take place
Priority Encoder Truth table
1 d d d
0 1 d d
0 0 1 d
0 0 0 1
0 0 0 0
I0
I1
I2
I3
0 0 1
0 1 1
1 0 1
1 1 1
d d 0
x y IST
x = I0' I1'
y = I0' I1 + I0’ I2’
(IST) = I0 + I1 + I2 + I3
Inputs
Outputs
Boolean functions
Priority Interrupt

## Slide 23: INTERRUPT CYCLE
At the end of each Instruction cycle
- CPU checks IEN and IST
- If IEN  IST = 1, CPU -> Interrupt Cycle
  SP SP - 1 Decrement stack pointer
  M[SP]  PC Push PC into stack
  INTACK  1 Enable interrupt acknowledge
  PC  VAD Transfer vector address to PC
  IEN  0 Disable further interrupts
  Go To Fetch to execute the first instruction
  in the interrupt service routine
Priority Interrupt

## Slide 24
Interrupt Service Routine
An interrupt handler, also known as an interrupt service routine (ISR), is a callback subroutine in an operating system whose execution is triggered by the reception of an interrupt. Interrupt handlers have a multitude of functions, which vary based on the reason the interrupt was generated.

## Slide 25: INTERRUPT SERVICE ROUTINE
Initial and Final Operations
Each interrupt service routine must have an initial and final set of
operations for controlling the registers in the hardware interrupt system
Initial Sequence
[1] Clear lower level Mask reg. bits
[2] IST <- 0
[3] Save contents of CPU registers
[4] IEN <- 1
[5] Go to Interrupt Service Routine
Final Sequence
[1] IEN <- 0
[2] Restore CPU registers
[3] Clear the bit in the Interrupt Reg
[4] Set lower level Mask reg. bits
[5] Restore return address, IEN <- 1
Priority Interrupt
address
Memory
JMP PTR
JMP RDR
JMP KBD
JMP DISK
0
1
2
3
I/O service programs
Program to service
magnetic disk
Program to service
line printer
Program to service
character reader
Program to service
keyboard
DISK
PTR
RDR
KBD
255
256
750
256
750
Stack
Main program
current instr.
749
KBD
interrupt
2
VAD=00000011
3
4
Disk
interrupt
5
6
7
8
9
10
11
1

## Slide 26: DIRECT MEMORY ACCESS
High-impedence
(disabled)
when BG is
enabled
CPU bus signals for DMA transfer
Block diagram of DMA controller
* Block of data transfer from high speed devices, Drum, Disk, Tape
* DMA controller - Interface which allows I/O transfer directly between
Memory and Device, freeing CPU for other tasks
* CPU initializes DMA Controller by sending memory
address and the block size(number of words)
Address bus
Data bus
Read
Write
ABUS
DBUS
RD
WR
Bus request
Bus granted
BR
BG
CPU
Address bus
Data bus
DMA select
Register select
Read
Write
Bus request
Bus grant
Interrupt
DS
RS
RD
WR
BR
BG
Interrupt
Data bus
buffers
Address bus
buffers
Address register
Word count register
Control register
DMA request
DMA acknowledge
to I/O device
Control
logic
Direct Memory Access
Internal Bus

## Slide 27
When BG =1, the CPU can communicate with the DMA registers.
When BG=0, CPU will give up the buses and DMA can directly communicate with the memory.
DMA controller has 3 registers like address register, word count register and control register.
The address register contains an address to specify the desired location in memory.
The word count register holds the number of words to be transferred.
The control register specifies the modes of transfer.

## Slide 28: DMA I/O OPERATION
Starting an I/O
- CPU executes instruction to
Load Memory Address Register
Load Word Counter
Load Function(Read or Write) to be performed
Issue a GO command
Upon receiving a GO Command DMA performs I/O
operation as follows independently from CPU
Input
[1] Input Device <- R (Read control signal)
[2] Buffer(DMA Controller) <- Input Byte; and
assembles the byte into a word until word is full
[4] M <- memory address, W(Write control signal)
[5] Address Reg <- Address Reg +1; WC(Word Counter) <- WC - 1
[6] If WC = 0, then Interrupt to acknowledge done, else go to [1]
Output
[1] M <- M Address, R
M Address R <- M Address R + 1, WC <- WC - 1
[2] Disassemble the word
[3] Buffer <- One byte; Output Device <- W, for all disassembled bytes
[4] If WC = 0, then Interrupt to acknowledge done, else go to [1]
Direct Memory Access

## Slide 29: CYCLE STEALING
While DMA I/O takes place, CPU is also executing instructions
DMA Controller and CPU both access Memory -> Memory Access Conflict
Memory Bus Controller
- Coordinating the activities of all devices requesting memory access
- Priority System
Memory accesses by CPU and DMA Controller are interwoven,
with the top priority given to DMA Controller
-> Cycle Stealing
Cycle Steal
- CPU is usually much faster than I/O(DMA), thus
CPU uses the most of the memory cycles
- DMA Controller steals the memory cycles from CPU
- For those stolen cycles, CPU remains idle
- For those slow CPU, DMA Controller may steal most of the memory
cycles which may cause CPU remain idle long time
Direct Memory Access

## Slide 30: DMA TRANSFER
BG
BR
CPU
RD
WR
Addr
Data
Interrupt
Random-access
memory unit (RAM)
RD
WR
Addr
Data
BR
BG
RD
WR
Addr
Data
Interrupt
DS
RS
DMA
Controller
I/O
Peripheral
device
DMA request
DMA ack.
Read control
Write control
Data bus
Address bus
Address
select
Direct Memory Access

## Slide 31: Reentrant code
A computer program or routine is described as reentrant if the routine can be re-entered while it is already running (i.e it can be safely executed concurrently).
To be reentrant, a computer program or routine:
  Must hold no static (or global) non-constant data.
  Must not return the address to static (or global) non-constant data.
  Must work only on the data provided to it by the caller.
  Must not modify its own code. (unless executing in its own unique thread storage)
  Must not call non-reentrant computer programs or routines.
Example of non-reentrant code
int g_var = 1;
int f()
{ g_var = g_var + 2;
return g_var;
}
int g()
{
return f() + 2;
}

## Slide 32
In the above, f depends on a non-constant global variable g_var; thus, if two threads execute it and access g_var concurrently, then the result varies depending on the timing of the execution. Hence, f is not reentrant. Neither is g; it calls f, which is not reentrant.
Example for reentrant code:
int f(int i)
{ return i + 2; }
int g(int i)
{ return f(i) + 2; }