## Slide 1: Bus Arbitration
If several units can generate requests for bus access simultaneously, the bus master (bus controller) needs a way to select one of the units. This selection process is called Bus arbitration
Three different arbitration schemes: (number of control lines, speed of bus controller)
  Daisy chaining
  Polling
  Independent requesting
Some bus systems combine several distinct arbitration techniques
Bus arbitration schemes usually try to balance two factors:
– Bus priority: the highest priority device should be serviced
first
– Fairness: Even the lowest priority device should never
be completely locked out from the bus.
Types of Arbitration:
static: (priority fixed) dynamic: (flexible priority)
- Daisy chaining - polling
- Parallel arbitration - Time slice
- Independent Requesting. -LRU/FIFO
- rotating daisy chain

## Slide 2
Daisy Chaining
Polling
Bus Controller
U1
U2
Un
…
Bus
Bus Request
Bus Busy
Poll
Count

## Slide 3: polling
Unit requests the bus via BUS request line.
In response, the Bus controller proceeds to generate a sequence of numbers on the poll-count lines.
Each unit compares to the unique address assigned to it.
When requesting unit finds the match, Bus Busy signal is activated.
In response, bus controller terminates the polling process and Ui connects to the bus.
Advantage: failure of one unit need not affect the other units.
Disadvantage: expensive because of more control lines. Number of units are limited based on the poll-count lines capability

## Slide 4: Independent Requesting
The bus controller determines priority, which is programmable.
Drawback: 2n Bus request and bus grant lines to control n devices, whereas daisy chaining requires 2 such lines and polling requires log2n lines approximately.
Bus Controller
U1
U2
Un
…
Bus
Bus Request1
Bus Busy
Bus Request2
Bus Request n
Bus Grant1
Bus Grant2
Bus Grant n

## Slide 5: What is a Bus?
A communication pathway connecting two or more devices and also provide the mechanisms for controlling the exchange of signals over the bus.
System bus comprises of data, address and control bus and handles the intrasystem communication.
Data bus
  Carries data
  Width is a key determinant of performance
  8, 16, 32, 64 bit
Address bus
  Identify the source or destination of data
  Bus width determines maximum memory capacity of system
  e.g. 16 bit address bus giving 64k address space
Control bus
  Control and timing information
    Memory read/write signal
    Interrupt request
    Clock signals

## Slide 6: Bus Interconnection Scheme
Types of Buses
• Today there are likely to be a number of different buses in the typical machine, supporting various devices. They can be divided into
– Local buses
• Such as PCI(Peripheral Component Interconnect)
• Used with internal devices such as graphical cards
-External buses
• Such as ISA(Industry Standard Architecture)
• Used with external devices such as scanners.
Other types of buses:
• Processor-Memory Bus
– Short and high speed
– Only need to match the memory system
- Maximize memory-to-processor bandwidth
– Connects directly to the processor
– Optimized for cache block transfers

## Slide 7: Bus Protocols
The essence of any bus is the set of rules by which data moves between devices. This set of rules is called a “protocol.
- PCI (Peripheral Component Interconnect)
- SCSI (Small computer System Interconnect)
PCI:
PCI bus is often referred as “local” bus which is designed to interface with different microprocessor families, main memory, and a very wide range of I/O devices.
It can support either 32- bit or 64- bit data transfer with maximum clock rate of 66 MHZ and allows a data transfer rate up to 524 MB/s.

## Slide 8: PCI BUS
Familiar with I/O bus and standard I/O interfaces─ parallel bus PCI (Peripheral Connect Interface) for a synchronous parallel communication interface bus
Devices connected to the PCI bus appear to the processor as if they were connected directly to the processor bus.
Early PC’s – 8 bit XT Bus
16-bit bus – ISA bus
32-bit – EISA bus
The PCI was developed as a low cost bus that is truly processor independent.
An important feature that the PCI is a plug-and-play capability for connecting I/O devices.
To connect a new device, the user simply connects the device interface board to the bus.

## Slide 10: PCI – Data Transfer Contd.,
The PCI is designed to support burst data transfer mode of operation and it uses multiplexed address and data lines.
Advantages:
  Speed.
  Reliability.
  Multiple masters.
  Configurability
The bus supports three independent address spaces
  Memory
  I/O
  Configuration
A 4-bit command that accompanies the address identifies which of the three spaces is being used in a given data transfer operation

## Slide 11
Before, The master maintains the address information on the bus until data transfer is completed. But this is not necessary
The address is needed only long enough for the slave to be selected.
The slave can store the address in its internal buffer.
Thus the address is needed for one clock cycle only, freeing the bus for sending the data in subsequent clock cycles => reduces cost
A master is called an initiator in PCI terminology – DMA controller.
The addressed device that responds to commands is target.

## Slide 12
Data transfer signals on the PCI bus
Name Function
CLK A 33-MHz or 66 MHz clock
FRAME# sent by initiator to indicate the duration of a transaction
AD 32 address/data lines (may be optionally increased to 64)
C/BE# 4 command/byte enable lines (8 for a 64- bit bus)
IRDY#, TRDY# Initiator ready and target ready signals
DEVSEL# a response from the device indicating that it has recognized its address and ready for a data transfer transaction
IDSEL# Initialization Device Select
Signals whose name ends with the symbol # are asserted when in the low voltage state

## Slide 13: A read operation on the PCI Bus

## Slide 14: Example of a Bus transaction
Processor reads 4 32-bit words from the memory.
Initiator – processor, target – memory
A complete transfer operation on the bus, involving an address and a burst of data is called transaction
Individual word transfers within transaction are called phases
Clock cycle 1 – FRAME# is asserted by the processor, address is sent on AD lines, a command on the C/BE# lines
Clock cycle 2 – AD bus lines are off => processor removes address from AD lines, DEVSEL# is asserted, C/BE# (4 lines are associated with one byte on the AD lines.

## Slide 15
The initiator sets one or more of the C/BE# lines to indicate which byte lines are used for transferring data
Clock cycle 3 – IRDY# is asserted to indicate that initiator is ready to receive the data, TRDY# - to indicate that target has data to send at this time.
The initiator loads the data into its input buffer at the end of the clock cycle.
Clock cycle 4 to 6 – target sends 3 more words
Frame# is negated during clock cycle 5
After sending the 4th word in CLK cycle 6, the target disconnect drivers and negates DEVSEL# at the beginning of CLK cycle 7.

## Slide 16: SCSI Bus
SCSI – Small Computer System Interface – defined by ANSI – X3.131 – pronounced as SCUZZY - is a set of standards for physically connecting and transferring data between computers and peripheral devices
Narrow bus – 8 data lines
Wide bus – 16 data lines
Earlier versions – High voltage differential (HVD) – 5V
Latest versions – Low voltage differential (LVD) – 3.3V
The maximum transfer rate in commercial devices – 5mb/s to 160mb/s
Maximum transfer rate of the standard – 320mb/s, 640mb/s.
The maximum transfer rate on a given bus is often a function of the length of the cable and the number of devices connected
SCSI is most commonly used for hard disks and tape drives, but it can connect a wide range of other devices, including scanners and CD drives.(8 or 16 devices can be attached to a single bus)

## Slide 17
The maximum capacity of the bus is 8 devices for a narrow bus and 16 devices for a wide bus.
This controller uses DMA to transfer data packets from the main memory to the device, or vice-versa. A packet may contain a block of data, commands from the processor to the device or status information about the device.
A controller connected to a SCSI bus is one of the two types – initiator or a target
An initiator has the ability to select a particular target and send commands specifying the operations to be performed.
Initiator – SCSI controller, target – disk controller
The initiator establishes a logical connection with the intended target