## Slide 1: BOOTH MULTIPLICATION

## Slide 2: Description and Hardware for Booth Multiplication
QR multiplier
Qn least significant bit of QR
Qn+1 previous least significant bit of QR
BR multiplicand
AC 0
SC number of bits in multiplier
Algorithm
Do SC times
QnQn+1 = 10
AC ← AC + BR + 1
QnQn+1 = 01
AC ← AC + BR
Arithmetic shift right AC& QR
SC ← SC – 1

## Slide 3: Flowchart for Booth Multiplication
Multiply
Multiplicand in BR
Multiplier in QR
AC ← 0
Qn+1 ← 0
SC ← n
QnQn+1
AC ← AC + BR + 1
AC ← AC + BR
ashr (AC & QR)
SC ← SC – 1
SC
= 0
≠ 0
= 01
= 10
= 00
= 11
END
AC
QR
Qn+1
SC
Comment
Example: -9 × -13 = 117
BR = 10111, BR + 1 = 01001
00000
10011
01001
01001
00100
11001
00010
01100
10111
11001
11100
10110
11110
01011
01001
00111
00011
10101
0
5
1
4
1
3
0
0
1
0
2
1
Subtract BR
Add BR
Subtract BR
Ashr
Ashr
Ashr
Ashr
Ashr

## Slide 4: Exercise
Show the step by step multiplication process using Booth algorithm when the following binary numbers are multiplied. Assume 5-bit registers that hold signed numbers. The multiplicand in both cases is +15.
  (+15) × (+13)
  (+15) × (-13)

## Slide 5: References
Text Book
M. M. Mano, Computer System Architecture, Prentice-Hall,2004