## Slide 1: challenges

## Slide 2: 1.heterogeneity
The Internet enables users to access services and run
applications over a heterogeneous collection of
computers and networks. Heterogeneity applies to
all of the following:
Networks
computer hardware
operating systems
programming languages
implementations by different developers

## Slide 3
The heterogeneity on the network protocols on the network is avoided by using internet protocol to communicate each other.
operating systems of all computers on the Internet need to include the Internet protocols, but do not necessarily provide the same API to these protocol.
Different programming languages use different representation of character and data structures, this need to be considered if these two programs need to be communicated.
Programs written by different developers cannot communicate with one another unless they use common standards.

## Slide 4: Middleware
Middleware applies to a software layer that provides a programming abstraction and masking the heterogeneity of the networks, hardware, operating systems and programming languages.
Ex:CORBA,RMI

## Slide 5
mobile code is used to refer to program code
that can be transferred from one computer to
another and run at the destination
  Ex: JAVA Applet
virtual machine approach provides a way of making code executable on a variety of host computers: the compiler for a particular language generates code for a virtual machine instead of a particular hardware code.
  Ex: JVM

## Slide 6: openness
The openness of distributed systems is determined primarily by the degree to which new resource-sharing services can be added and be made available for use by a variety of client programs.
Systems designed to support resource sharing are termed as open distributed systems.
Implemented at the hardware level by the addition of computers to the network and,
At the software level by the introduction of new services and the reimplementation of old ones.

## Slide 7: Security
Three components:
Confidentiality: protection against disclosure to unauthorized individuals.
Integrity : protection against alteration or corruption
Availability : protection against interference to access the resources

## Slide 8
In a distributed system, clients send requests to access data managed by servers, which involves sending information in messages over a network.
The server needs to know that the user is really the intended , and the server needs to be sure of the identity of the user to whom they are dealing.
These challenges can be met by the use of encryption techniques.

## Slide 9: Security challenges have not yet avoided
Denial of service attacks: This security problem is that a user tries to disrupt a service by bombarding the service with a large number of pointless requests and making the serious users unable to use it.
Security of mobile code: Consider someone who receives an executable program as an electronic mail attachment with some picture. but in reality it may access local resources

## Slide 10: Scalability
A system is described as scalable if it will remain effective when there is a significant increase in the number of resources and the number of users.

## Slide 11: Challenges with the design of scalable distributed system
Controlling the cost of physical resources:
  The frequency of accessing in an intranet is likely to grow as the number of users and computers increases.
  It must be possible to add server computers to avoid the performance bottleneck.
  In general, If a system with n users requires to be scalable needs support of at most O(n) physical resources.

## Slide 12
Controlling the performance loss:
  Consider the table maintains domain name and its corresponding Internet address.
  If the entry increases, there is possibility of performance loss.
  The time taken to access hierarchically structured data is O(log n), where n is the size of the set of data.
  For a system to be scalable, the maximum performance loss should be no worse than this.

## Slide 13
Preventing software resources running out:
  It is difficult to predict the demand that will be put on a system years ahead.
  Moreover, overcompensating for future growth may be worse than adapting to a change when we are forced to larger Internet.

## Slide 14: Failure handling
Failures in a distributed system are partial – that is, some components fail while others continue to function.
Therefore the handling of failures is difficult.
Detecting failures:
  some failures can be detected. Some failures are difficult or even impossible to detect such as a remote crashed server in the Internet.

## Slide 15
Masking failures:
  Some failures that have been detected can be hidden or made less severe.
Two examples of hiding failures
1. Messages can be retransmitted when they fail to arrive.
2. File data can be written to a pair of disks so that if one is corrupted, the other may still be correct.

## Slide 16
Tolerate the failure:
  For example, when a web browser cannot contact a web server, it does not make the user wait for ever while it keeps on trying.
  It informs the user about the problem and leaving them free to try again later.