## Slide 1: Asynchronous Counter Operation

## Slide 2: Introduction: Counters
Counters are circuits that cycle through a specified number of states.
Two types of counters:
  synchronous (parallel) counters
  asynchronous (ripple) counters
Ripple counters allow some flip-flop outputs to be used as a source of clock for other flip-flops.
Synchronous counters apply the same clock to all flip-flops.

## Slide 3: Asynchronous (Ripple) Counters
Asynchronous counters: the flip-flops do not change states at exactly the same time as they do not have a common clock pulse.
Also known as ripple counters, as the input clock pulse “ripples” through the counter – cumulative delay is a drawback.
n flip-flops  a MOD (modulus) 2n counter. (Note: A MOD-x counter cycles through x states.)
Output of the last flip-flop (MSB) divides the input clock frequency by the MOD number of the counter, hence a counter is also a frequency divider.

## Slide 4: Asyn. Counters with MOD no. < 2n
States may be skipped resulting in a truncated sequence.
Technique: force counter to recycle before going through all of the states in the binary sequence.
Example: Given the following circuit, determine the counting sequence (and hence the modulus no.)
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
C
B
A
B
C
All J, K inputs are 1 (HIGH).

## Slide 5: Asynchronous Counter Operation
Asynchronous binary counter
  2-bit asynchronous binary counter
  3-bit asynchronous binary counter
  4-bit asynchronous binary counter
Asynchronous decade counter

## Slide 6: Asynchronous Counter Operation
2-bit asynchronous binary counter

## Slide 7: Asynchronous Counter Operation
3-bit asynchronous binary counter

## Slide 8: Asynchronous Counter Operation
4-bit asynchronous binary counter

## Slide 9: Asynchronous Counter Operation
Asynchronous decade counter

## Slide 10: Asyn. Counters with MOD no. < 2n
Example (cont’d):
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
C
B
A
B
C
All J, K inputs are 1 (HIGH).
A
B
1
2
C
NAND
Output
1
0
3
4
5
6
7
8
9
10
11
12
Clock
MOD-6 counter produced by clearing (a MOD-8 binary counter) when count of six (110) occurs.